## Slide 1: 5 stages pipelined MIPS Architecture
Εργασία Ψηφιακών Συστημάτων
Χρήστος Ντούμας
Α.Ε.Μ.: 10095

## Slide 2
MIPS Overview
A pipeline is a technique used to improve processor performance by overlapping the execution of multiple instructions. Each instruction goes through a series of stages (like fetching, decoding, executing, memory access, and writing back).
The "without interlocked pipeline stages" part means the MIPS architecture, in its original form, didn't have hardware mechanisms to automatically handle situations where one instruction's output was needed as input by a later instruction in the pipeline (data hazards). Instead, the compiler was responsible for scheduling instructions to avoid these conflicts.
MIPS is a RISC architecture, meaning it uses a smaller, simpler set of instructions compared to Complex Instruction Set Computing (CISC) architectures like x86.
MIPS, which stands for Microprocessor without Interlocked Pipeline Stages, is a type of microprocessor architecture using 32 bits instructions. It's a core component of the Reduced Instruction Set Computing (RISC) approach, known for its focus on simplicity and speed. MIPS processors are designed to execute simple instructions in a single clock cycle, utilizing a pipeline to overlap different stages of instruction execution.

## Slide 3: Basic design overview
Fetch
Decode
Execute
Memory
Write
back

## Slide 4
Theoretical analysis
  The main components of the MIPS architecture are:
  Instruction Memory
  Register file
  Decoders
  Sign Extension
  Control Unit
  There are also 3 types of hazards in this architecture:
  Structural Hazards
  Control Hazards
  Data Hazards
Components
Hazards
  There are 3 types of instructions that are being used in a MIPS architecture:
  R-type (add, sub, or, slt)
  I-type (addi, lw)
  J-type (used for jump/branch)
Instructions

## Slide 5
Theoretical analysis (Instructions)
R-type
Op(6 bits) | Rs (5 bits) | Rt (5 bits) | Rd (5 bits) | Shamt (5 bits) | Funct (6 bits)
Operation code. Always 0 in R-type instructions. Operation is defined by funct | First source register | Second source register | Destination register. The result will be stored here | Shift amount. Used in only in logical shifting instructions | Function code. Determines the operation that will be performed in the ALU
Example
Add $t0, $t1, $t2
000000 | 01001 | 01010 | 01000 | 00000 | 100000

## Slide 6
Theoretical analysis (Instructions)
I-type
Addi $t0, $t1, 5
Op(6 bits) | Rs (5 bits) | Rt (5 bits) | Immediate (16 bits)
Operation code. Specifies the type of operation (addi, lw, beq etc.) | Source register | Destination register | Constant value or offset (signed or unsigned) depending the instruction
001000 | 01001 | 01000 | 0000000000000101
Example

## Slide 7
Theoretical analysis (Instructions)
J-type
j 0x00400020
Op (6 bits) | Address (26 bit)
Operation code | Target address
000010 | 0x00100008
Example

## Slide 8
Theoretical analysis (Components)
Instruction Memory
It’s a read-only memory (ROM) that stores the hexadecimal values of the instructions that are going to be executed.
addi x5, x0, 5 # x5 = 5 (I-type)
addi x6, x0, 3 # x6 = 3
add x7, x5, x6 # x7 = x5 + x6 = 8 (R-type)
lw x8, 0(x0) # Load word from x0 to x8
addi x9, x0, 1 # x9 = 1
add x10, x8, x9 # x10 = x8 + 1

## Slide 9
Theoretical analysis (Components)
  Corrects the format of a regular 32-bit instruction to an I-type instruction and incorporates signed numbers format for immediate operations.
  Produces the signals needed for each operation and defines how data will move around between memory, registers and the ALU.
Sign extension
Control Unit
  Contains 32 general purpose 32-bit registers. By consensus, register x0 is initialized to 0 and cannot be written.
Register File

## Slide 10
Theoretical analysis (Components)
ALU Decoder
Decodes the instructions for specific ALU operations
Main Decoder
Decodes the instructions for the rest of the operations

## Slide 11
Design Datapath

## Slide 12
Theoretical analysis (Hazards)
  They occur due to branch or jump instructions. The processor doesn't know which instruction to fetch next because it hasn’t resolved if the branch was taken or not.
  Solutions:
  Branch prediction
  Delayed Branch
  Stalling
  Speculative execution
  They take place when an
  Instruction depends on the
  result of a previous instruction
  that hasn’t completed yet.
  Solutions:
  Forwarding
  Stalling
  Compiler scheduling
Control Hazard
Data Hazard
  They happens when hardware
  resources are insufficient to
  handle all the instructions in
  the pipeline at once.
  E.g.: Two instructions want to
  access memory at once. One
  for fetch and on for load.
  Solutions:
  Hardware duplication
  Stalling
  Scheduling
Structural Hazard

## Slide 13: Improved Design

## Slide 14: Forwarding logic
Control Signal | Source | Explanation
ForwardA = 00 | Decode/Execute cycle | The first operand comes from the register file.
ForwardA = 10 | Execute/Memory cycle | The first operand is forwarded from the prior ALU result.
ForwardA = 01 | Memory/Writeback cycle | The first operand is forwarded from data memory or earlier ALU result.
ForwardB = 00 | Decode/Execute cycle | The second operand comes from the register file.
ForwardB = 10 | Execute/Memory cycle | The second operand is forwarded from the prior ALU result.
ForwardB = 01 | Memory/Writeback cycle | The second operand is forwarded from data memory or earlier ALU result.

## Slide 15: Results

## Slide 16: Next Steps
Increase the number of instructions supported from the ALU
Add a jump instruction
Improve the hazard unit to handle all kind of hazards (Structural and control)
Make the design synthesizable

## Slide 17: Thank you